## Slide 1: Towards a Collision Free Medium Access For QoS Support in WLAN
Prepared By
Muhaimenul Islam (134414) Fahmid Shahriar (134419)
Supervised By
Ashraful Alam Khan
Assistant Professor
Islamic University of Technology

## Slide 2: Outline
Introduction
EDCA Background
Problem
Existing Solution
Our Goal
Solution
Conclusion

## Slide 3: Introduction
Medium access control in WLAN is a great overhead to ensure a better throughput in a wireless medium
Overhead of DIFS and exponential back-off based CW significantly decrease MAC sub-layer efficiency.
New emerging applications requires QoS-constrained traffic at variable rates
Efficient medium access control protocol is necessary to cope up with these challenges.
600 Mbps
H
I
G
H
HIGH
LOW

## Slide 4: EDCA Background
Introduction of access categories for the QoS support
Multiple back-off entities with different priorities in parallel
Different AIFS , TXOP, RC for different categories to maintain the priority.

## Slide 5: EDCA Background (Cont.)

## Slide 6: Problem with EDCA
Different access categories may collide with each other
Lots of idle time
Probability of collision is still high
Channel access mechanism is randomized

## Slide 7: Problem with EDCA (Cont.)
A
B
DATA
DATA
AIFS[H]
AIFS[L]
AIFS[H]
AIFS[L]
4
5
6
4
8
8

## Slide 8: Existing Solutions
Co-ordination based Scheme:
Central coordinator fixed the schedule
Disadvantage:
Single point of failure
Requires extra infrastructure
Slot-assignment scheme: TON_2017 ,[5] [9]
Reserve slots for transmission
Combine TDMA and CSMA approach
Disadvantage:
Global Synchronization needed
Learning and set up phase for scheduling
Vulnerable to slot drifts

## Slide 9: Existing Solutions
Multi-frequency assisted schemes
Total frequency is divided into different subcarriers
Each node is assigned with a different subcarrier
Dual Antenna Method [2]
Receiver based Method [1]
Disadvantage:
Costly infrastructure
Limited scalability

## Slide 10: Our Goal
Reduce the probability of collision using a effective back-off process
Reduce the idle time
Ensuring priority access
Gain a better convergence speed to steady date
Without-
  Centralized support
  Additional frequency and hardware Infrastructure

## Slide 11: Proposed Solution
Modified deterministic back-off for different access categories
Multiplicative approach for collision
Special retry counter for detecting the congested scenario

## Slide 12: Reducing the probability of collision ( Modified Deterministic back-off)
Different access categories will use deterministic back-off value after successful transmission.
The range for the back-off value for different categories will be different.
A station with a deterministic back-off value will never collide with the same genre .

## Slide 13: Reducing the probability of collision ( Modified Deterministic back-off) Cont.
5
10
15
0
A
B
C
D
E

## Slide 14: Use of multiplicative approach:
To ensure fair and prioritize channel access
In the case of collision , the increase of the deterministic back-off value will be multiplicative to the minimum value chosen from the first success.
So in a non-congested scenario two nodes from different categories with same genre will not collide.
Successful periodical transmission is achieved using the proposed back-off process

## Slide 15: Cont.
3
9
12
6
A[H] A[L]
B[H] B[L]
R

## Slide 16: Reducing the idle time (Retry Counter)
In a non-congested scenario, deterministic node can collide with the random ones
Unnecessary jump to a greater deterministic back-off value due to collision
The collided node will wait for a sudden limit and use the same deterministic back-off value
After reaching the limit, the deterministic back-off value will be increased using the proposed multiplicative back-off process

## Slide 17: Faster convergence to a collision-free schedule
A learning phase from the beginning of the active period.
Try to identify the number of nodes in the collision domain using MAC layer packet format
In a congested scenario, during collision jump to a suitable back-off value for avoiding collision using the learning phase.

## Slide 18: Conclusion
Performance measure in NS3 simulator
Comparison between Standard EDCA with Ours method
  Effect on Throughput
  Effect on Collusion Probability
  End to End Delay

## Slide 19
Performance Evaluation
Chart: Through vs # of Stations
| 2 | 5 | 8 | 10
EDCA | 4.7 | 3.5 | 1.5 | 0.5
Proposed | 4.9 | 4.4 | 2.8 | 1.8
11/8/17
19

## Slide 20: References
[1] Sheeraz A.Alvi1, Adeel Baig, Kashif Sattar2, “Frequency-Domain Backoff Mechanism for OFDM-Based Wireless LANs” [2016]
[2] Souvik Sen, Romit Roy Choudhury, Srihari Nelakuditi “No Time to Countdown:Migrating Backoff to the Frequency Domain” [2014]
[3] Sanabria-Russo, Luis, et al. "A high efficiency MAC protocol for WLANs: Providing fairness in dense scenarios." IEEE/ACM Transactions on Networking (TON) 25.1 (2017): 492-505.
[4] Haitao Zhao , JiboWei , NurulISarkar , ShengchunHuang “E-MAC: An evolutionary solution for collision avoidance in wireless ad hoc networks” [2016]

## Slide 21: References
[5] M. F. Tuysuz · H. A. Mantar, “A Beacon-Based Collision-Free Channel Access Scheme for IEEE 802.11 WLANs” [2015]
[6] George W. Wong and Robert W. Donaldson, “Improving the QoS Performance of EDCF in IEEE 802.11e Wireless LANs”
[7] Yan Zhang, Loukas Lazos, Kai Chen, Bocan Hu, and Swetha Shivaramaiah, “Multi-Channel Medium Access without Control Channels: A Full Duplex MAC Design” IEEE, 2017
[8] Boris Bellalta , Luciano Bononib, affaele Brunoc, Andreas Kassler, ‘‘Next generation IEEE 802.11 Wireless Local Area Networks:Current status, future directions and open challenges” [2015]
[9] “Winning the Lottery: Learning Perfect Coordination with Minimal Feedback” , Globecom 2013 - Wireless Communications Symposium

## Slide 22: Thank You